## Slide 1: TWAMP Server/Reflector
implemented in bmv2
Damian Parniewicz, May 2020

## Slide 2: TWAMP development and testing environment
p4app docker (Mininet)
Host
Switch DP - bmv2
TWAMP Reflector (P4)
CPU Loopback iface
(veth)
TWAMP Client/Sender (Python)
Switch CPU - namespace
TWAMP
Server
(Python)
10.0.0.254:862
10.0.0.253: 8975
10.0.0.254: 8975
TWAMP control
TWAMP test
Port #1
Port #2
10.0.1.1
P4 code of TWAMP Reflector for V1model.p4
Simple TWAMP Server running with standard Linux TCP/IP stack
  No CPU header in messages between Switch DP and Switch CPU
  Handle TCP handshake
  Strict forward re-implementation of twamp-server.go
twampy.py and twping as clients for testing
  TWAMP solution works for any client IP address
python3 twampy.py controller
10.0.0.254:862 10.0.1.1:20001 -c 10
Topo.py
twping 10.0.0.254 -c 10

## Slide 3: Main control blocks of TWAMP bmv2 solution
ARP respond control:
  Enable CPU Looback and TWAMP reflector by providing their MAC addresses
CPU Loopback control:
  Forward packets to/from the Switch CPU
  A most simple working solution by proxying of Ethernet MAC addresses
TWAMP Reflector control:
  Responds TWAMP Test messages back to the client
Switch DP - bmv2
TWAMP Reflector control (P4)
CPU Loopack control (P4)
ARP respond control (P4)
Switch CPU
Loopback iface (veth)
Parser
Deparser
Checksum

## Slide 4: ARP respond control
Switch - bmv2
TWAMP Reflector control (P4)
CPU Loopack control (P4)
ARP respond control (P4)
Responding with:
  CPU MAC address
  DP MAC address to CPU (instead of MAC of the TWAMP client)
  TWAMP Reflector MAC address
ARP respond control (switch)
Who has 10.0.0.253?
10.0.0.254 is f6:61:c0:6a:14:66
TWAMP Client/Sender (Host)
TWAMP
Server
(CPU)
CPU_MAC: f6:61:c0:6a:14:66
CPU_IP: 10.0.0.254/24
Who has 10.0.1.1?
00:00:00:00:01:01
10.0.0.1.1/24
10.0.1.1 is f6:61:c0:6a:00:77
Who has 10.0.0.254?
DP_MAC: f6:61:c0:6a:00:77
10.0.0.253 is f6:61:c0:6a:00:77
TWAMP_REFLECTOR_IP:
10.0.0.253/24
ARP responder lookup table:
IP:10.0.0.254 => send_arp_reply(MAC: f6:61:c0:6a:14:66)
IP:10.0.0.253 => send_arp_reply(MAC: f6:61:c0:6a:00:77)

## Slide 5: CPU Loopback control
Forward to CPU if packet dstIP is CPU IP
  Host MAC and ingress_port stored per srcIP in loopback hash tables
Forward packet from CPU to hosts
  Look up host MAC and egress port for dstIP from loopback hash tables
CPU Loopback control (switch)
TWAMP Client/Sender (Host)
TWAMP
Server
(CPU)
Switch - bmv2
TWAMP Reflector control (P4)
CPU Loopack control (P4)
ARP respond control (P4)
TCP packet:
SMAC 00:00:00:00:01:01
DMAC f6:61:c0:6a:14:66
src IP: 10.0.1.1, dst IP: 10.0.0.254
TCP packet:
SMAC: f6:61:c0:6a:14:66
DMAC 00:00:00:00:01:01
src IP: 10.0.0.254, dst IP: 10.0.1.1
TCP packet:
SMAC: f6:61:c0:6a:14:66
DMAC f6:61:c0:6a:00:77
src IP: 10.0.0.254, dst IP: 10.0.1.1
Hash Register:
IP:10.0.1.1 => MAC: 00:00:00:00:01:01, port: 1
00:00:00:00:01:01
10.0.0.1.1/24
f6:61:c0:6a:14:66
10.0.0.254/24
f6:61:c0:6a:00:77
TCP packet:
SMAC f6:61:c0:6a:00:77
DMAC f6:61:c0:6a:14:66
src IP: 10.0.1.1, dst IP: 10.0.0.254

## Slide 6: TWAMP Reflector control
Symmetrical TWAMP Test messages
TWAMP Reflector port number hardcoded in P4 Parser
TWAMP Reflector IP and MAC doesn’t matter (existence emulated only by P4 code)
TWAMP Reflector control (switch)
TWAMP Client/Sender (Host)
Switch - bmv2
TWAMP Reflector control (P4)
CPU Loopack control (P4)
ARP respond control (P4)
UDP packet:
SMAC 00:00:00:00:01:01
DMAC f6:61:c0:6a:00:77
src IP: 10.0.1.1, dst IP: 10.0.0.253
UDP packet:
SMAC: f6:61:c0:6a:00:77
DMAC 00:00:00:00:01:01
src IP: 10.0.0.253, dst IP: 10.0.1.1
test session table:
configure(REFLECTOR_IP: 10.0.0.253, REFLECTOR_MAC: 10.0.0.253,
SENDER_IP: 10.0.1.1, SENDER_PORT: 20001)
00:00:00:00:01:01
10.0.0.1.1/24
DP_MAC: f6:61:c0:6a:00:77
TWAMP_REFLECTOR:
10.0.0.253:8975
TWAMP
Server
(CPU)
header twamp_test_t {
bit<32> sequenceNumber;
bit<64> timestamp;
bit<16> errorEstimate;
bit<16> mbz0;
bit<64> receiveTimestamp;
bit<32> senderSequenceNumber;
bit<64> senderTimestamp;
bit<16> senderErrorEstimate;
bit<16> mbz1;
bit<8> senderTTL;
}
python3 twampy.py sender 10.0.0.253:8975 -c 10
Add/remove entries in TWAMP test session table

## Slide 7: Limitation related to NTP Timestamp
bmv2 timestamp is an number of microseconds from bmv2 switch start
  a number of seconds approximated by bit shift operation >>20
  `Topo.py` script set an number of seconds from 1th Jan 1900 to bmv2 start time in a bmv2 register
a NTP second fraction (float) is always zero
  Barefoot Tofino has different timestamp system so no big sense to prepare workaround for this problem in bmv2